## Slide 1
Coverage Breakdown(Venn Diagram) select count(distinct material) from workspace.default.output --591
select count(distinct material_id) from workspace.default.routings --1392
Routing is a master-data set → it typically includes all possible materials
Production data is transactional → it only shows what was actually produced in the selected period.
category | material_count | percentage_of_total
In Both (Produced + Routing) | 591 | 42.46.00
Routing Only | 801 | 57.54.00

## Slide 2: 1. Routing Variability Analysis
Dynamically pivot routing parameters (setup_time_mins, cycle_time_sec, labour_time_sec) across plants.
You identify materials with inconsistent routing setups across sites.
Supporting puzzled faces—why identical materials are treated differently.

## Slide 3
order_id | material_id | plant_id | line | id | setup_time_mins | cycle_time_sec | labour_time_sec
411362 | 7835283 | 1 | 97 | 1 | 28 | 10.909 | 03.06
248157 | 7835283 | 1 | 97 | 1 | 28 | 11.25 | 3.713
497698 | 7835283 | 1 | 97 | 1 | 28 | 10.909 | 03.06
356503 | 7835283 | 4 | 106 | 1 | 30 | 11.25 | 5.625
356507 | 7835283 | 4 | 106 | 1 | 30 | 11.25 | 5.625
356502 | 7835283 | 4 | 106 | 1 | 30 | 11.25 | 5.625
275840 | 7835283 | 4 | 106 | 3 | 30 | 12.857 | 6.429
184236 | 7835283 | 1 | 105 | 7 | 28 | 12 | 3.96
275857 | 7835283 | 4 | 106 | 9 | 30 | 11.25 | 5.625
Key Question:Are routing standards (setup, cycle, labour) consistent across plants/lines/orders? Considering id = operation step.
Variations can occur across plants, within the same plant ,same lines, or across orders.
Leaves open interpretation whether differences are due to real process differences or data quality issues.
order_id | material_id | plant_id | line | id | setup_time_mins | cycle_time_sec | labour_time_sec
283328 | 7839956 | 1 | 93 | 1 | 37 | 7.448 | 2.458
353023 | 7839956 | 1 | 91 | 13 | 37 | 7.448 | 2.458
202000 | 7839956 | 1 | 93 | 22 | 37 | 7.448 | 2.458
235035 | 7839956 | 1 | 93 | 1 | 37 | 7.448 | 2.458
330036 | 7839956 | 3 | 79 | 1 | 46 | 9.418 | 9.418
357493 | 7839956 | 3 | 79 | 1 | 46 | 9.418 | 9.418
383708 | 7839956 | 3 | 57 | 1 | 46 | 9.418 | 9.418
247594 | 7839956 | 4 | 104 | 7 | 44 | 07.02 | 06.03
247219 | 7839956 | 4 | 104 | 7 | 44 | 07.02 | 06.03

## Slide 4
production_order | material | plant | line | linetype | expected_output | actual_gross_production_time | actual_net_production_time
330036 | 7839956 | 3 | 79 | 112B | 692721 | 1087655 | 745655
283328 | 7839956 | 1 | 93 | 2016P | 60100563 | 74804840 | 44464870
Order 283328 (Plant 1, Line 93):
  Massive production run
  ~12,351 hours of net production
  Indicates a long-duration, high-volume operation
Order 330036 (Plant 3, Line 79):
  Much shorter run
  ~207 hours of net production
  Suggests a smaller batch or faster turnaround
Despite both using the same material and routing ID, the scale and duration of production are vastly different. Plant 1 handles larger orders with lower hourly efficiency, while Plant 3 runs shorter, more efficient batches.

## Slide 5
Routing vs. Execution: even with the same routing ID, execution varies by plant and line.
Linetype Influence: linetype affects throughput and efficiency.
Factors |  |  | 
Machine Type | Older CNC | Newer robotic cell | 
Operator Skill | Junior staff | Experienced team | 
Shift Pattern | Mixed shifts | Dedicated day shift | 
Environmental Conditions | Humid | Climate-controlled | 
Hypothesis can be

## Slide 6
🤔 Puzzled Faces
Where things didn’t add up
  Same material, same routing ID—but vastly different results across sites
  Inconsistent cycle times and rate accuracy hint at deeper process variability
  Some lines had high setup times but low output, raising questions
“These puzzled expressions ask: Why does identical planning yield such different outcomes?”
😊 Happy Face: What’s Working Well
High throughput in some plants shows that optimized execution is possible.
😟 Sad Face: What’s Not Working
Same routing ID, different setup parameters → lack of standardization across plants.
Lower throughput in some plants despite similar routing plans suggests inefficiencies or missed opportunities.
Long durations with low output hint at idle time, poor scheduling, or resource constraints.